4. GPIO programming: Assume that BASE is the base address of a GPIO, and the GPIO registers are at the offset addresses IODIR, IOSET, IOCLR, IOPIN. The following shows how to define them as constants in ARM assembly code and C.
.set BASE, 0x101E4000 // #define BASE 0x101E4000
.set IODIR, 0x000 // #define IODIR 0x000
.set IOSET, 0x004 // #define IOSET 0x004
.set IOCLR, 0x008 // #define IOCLR 0x008
.set IOPIN, 0x00C // #define IOPIN 0x00C
Write a GPIO control program in both assembly and C to perform the following tasks.
(1). Program the GPIO pins as specified in Sect. 2.8.1.
(2). Determine the state of the GPIO pins.
(3). Modify the control program to make the LED blink while the input switch is closed.
I can’t simulate this but I think it would be something like this:

**Note: Base adress for the GPIO0 registers is 0x101E4000, where we have 4, 32 bit registers, each bit is 1 IO pin
IODIR(Base + 0): set pin as input (0) or output (1)
IOSET(Base + 4 bytes): set pin as high/3.3V (1)
IOCLR(Base + 8 bytes): set pin as low/gnd/0V (1)
IOPIN(Base + 12 bytes): read pin status, low(0) or high(1)
-Program: Simple code which sets pin0 as input and pin1 as output. pin0 is connected to a switch which is low in rest and high when is being pressed. pin1 is connected to the positive pin of a 3.3V led. The negative of the led is connected to gnd. If the switch is being pressed (pin0 = 1) then the led turns on (set pin1 to high).
The assembly code I think it shold be something like this:

*****Assembly program****

.textxp
.global start

start:
ldr sp, =stack_top
mov r0, BASE	//use r0 as Base adress
mov r1, #2	//r1 = 2 = 0010 (lower 4 bits), pin0 = 0, pin1 = 1. the others (p2 to p31) are 0
str r1, [r0, #IODIR]	//r1(..0010) to IODIOR, pin1 = output, pin0 (and p2 to 31) inputs.
str r1, [r0, #IOCLR]	//r1 to IOCLR, set pin1 as low
turn_off:
mov r1, #0	//r1 = 0
str r1, [r0, #IOSET]	//No pins are high (IOSET = 0x00000000)
loop:	//Checks input p0 by polling
ldr r1, [r0, #IOPIN]	//r1 = get IOPIN, pin values
tst r1, #1	// test ( same as ands) r1 && 0x01, same as IOPIN && 0x01, and modify flags values, tests if pin0 is 1
BNE turn_off	// If not (BNE, If not equals), goes back to turning of the led
mov r1, #2	//else, r1 = 2 = …0010
str r1, [r0, #IOSET]	//store r1 to IOSET, sets pin1 as high (3.3v) turning ON the led
bl loop	//goes back to loop

.data
.set BASE, 0x101E4000	//define Base 0x101E4000
.set IODIR, 0x000
.set IOSET, 0x004
.set IOCLR, 0x008
.set IOPIN, 0x00C

**Note: I’m not very confident about the C code. Very few examples (most of them very hard to understand) about how to use C for modifiying memory directly.
********C Code*******

#define BASE 0x101E4000
#define IODIR 0x000
#define IOSET 0x004
#define IOCLR 0x008
#define IOPIN 0x00C

void main(){
unsigned int base = (unsigned int *) BASE;	//*base = valor, escribe en base.	valor = *base, lee de base
*(base+IODIR) = 0x02	//sets pin1 as output, the others as inputs
*(base+IOSET) = 0	//no pins set as high
*(base+IOCLR) = 0x02	//set pin1 as low
while(1){
if( *(base + IOPIN) && 0x01 ){	//same as tst 0x01, pin0 is 1, switch pressed
*(base+IOSET) = 0x02	//pin1 set as high
}
else *(base+IOSET) = 0	//if not, pin1 set as low
}
}

**Note: I’m not very confident about the C code. Very few examples (most of them very hard to understand) about how to use C for modifiying memory directly.
********C Code*******

#define BASE 0x101E4000
#define IODIR 0x000
#define IOSET 0x004
#define IOCLR 0x008
#define IOPIN 0x00C

void main(){
unsigned int base = (unsigned int *) BASE;	//*base = valor, escribe en base.	valor = *base, lee de base
*(base+IODIR) = 0x02	//sets pin1 as output, the others as inputs
*(base+IOSET) = 0	//no pins set as high
*(base+IOCLR) = 0x02	//set pin1 as low
while(1){
if( *(base + IOPIN) && 0x01 ){	//same as tst 0x01, pin0 is 1, switch pressed
*(base+IOSET) = 0x02	//pin1 set as high
}
else *(base+IOSET) = 0	//if not, pin1 set as low
}
}